## Slide 1: Lecture 3 – Number Systems Part 2
Dr. Paul Hayes

## Slide 2
Number Systems and Arithmetic
Hexadecimal Systems for numbers:
The alphabet consists of the following {0-9, A,B,C,D,E,F}
Again the system is a positional system, example,
28 = (2 * 16 ^1) + (8 * 16^0)
28 = (32) + (8)
28 = 40
AF = (10 *16^1) + (15 * 16^0 )
AF = 175

## Slide 3
Number Systems and Arithmetic
Convert the following Hexadecimal numbers into
decimal numbers:
30
3F
45F
90ED
48
63
1119
37101
To Do

## Slide 4
Number Systems and Arithmetic
Converting from Decimal to Hex:
Keep dividing by 16, noting the remainder until the quotient is 0.
Example 54401,
54401 / 16 = 3400 R1
3400 / 16 = 212 R8
212 / 16 = 13 R4
13 / 16 = 0 R13
0
=> 54401 = D481

## Slide 5
Number Systems and Arithmetic
Examples of Converting from Decimal to Hex:
32
55
457
10001
27
20
37
1C9
2711
1B
To Do

## Slide 6
Number Systems and Arithmetic
Converting from Binary to HEX:
Simple conversion.
Step 1: Divide the binary number into segments of four bits.
Step 2: Read of the representation in HEX using HEX alphabet.
Example: 10011111
=> 1001 1111
=> 9 F
=> 9F
To Convert back from HEX to
binary we simply reverse the
procedure.

## Slide 7
Number Systems and Arithmetic
Octal Number System:
Alphabet L = {0,1,2,3,4,5,6,7}
Convert into Decimal: Positional conversion
  Example: 127 base 8 = 87 base 10
Convert into Binary: 3 bits complete the alphabet
  Separate out the binary number into segments of three bits and read off the Octal representation.
Reverse the procedure for conversion from Octal into Binary.

## Slide 8
Number Systems and Arithmetic
Why Octal and HEX:
As previously mentioned, all
computers and digital systems
use the binary representation.
The Octal and Hexadecimal
systems are very useful for
representing binary quantities
indirectly as their bases are powers
of two.
This implies that one Octal
number is represented as three
bits and a Hex number is
represented as four bits

## Slide 9
Number Systems
Dec | Hex | Oct | Bin
0 1 2 3 4 5 6 7 8 9 10 11 12 13 14 15 | 0 1 2 3 4 5 6 7 8 9 A B C D E F | 000 001 002 003 004 005 006 007 010 011 012 013 014 015 016 017 | 00000000 00000001 00000010 00000011 00000100 00000101 00000110 00000111 00001000 00001001 00001010 00001011 00001100 00001101 00001110 00001111

## Slide 10
Binary Addition Rules:
0 + 0 = 0
1 + 0 = 1
0 + 1 = 1
1 + 1 = 0 (Carry the 1)
Number Systems and Arithmetic

## Slide 11
Example binary addition:
1001 + 0110
=> 1001
=> + 0110
1111
10110 + 10111
=> 10110
=> + 10111
101101
Number Systems and Arithmetic

## Slide 12
Binary Subtraction Rules:
0 - 0 = 0
1 - 0 = 1
1 - 1 = 0
0 - 1 = 0 (But must borrow from higher column)
Number Systems and Arithmetic

## Slide 13
Example binary subtraction:
10110 - 10010
=> 10110
=> - 10010
00100
10110 - 10011
=> 10110
=> - 10011
00011
Number Systems and Arithmetic

## Slide 14
Example binary multiplication
1011
X 101
1011
0000
1011
______
110111
Number Systems and Arithmetic
How does a Computer Divide?
<http://mathforum.org/library/drmath/view/54338.html>

## Slide 15
Negative Numbers:
To represent negative numbers we use Two’s complement,
which is an 8 bit representation.
How?
Invert all the bits: 0->1, 1->0
Add 1
Example: to get -1,
1 (decimal) = 00000001 (binary)
Number Systems and Arithmetic

## Slide 16
Invert all the bits: 11111110
Add 1 : 11111111
Using TC -1 = 11111111
Using TC notation, the most significant bit indicates the sign. 1
means a negative number. With 8 bits we can represent signed
numbers in the range of:
127 0 -128
01111111 00000000 10000000
Number Systems and Arithmetic
Show Examples on Calculator
What is -4?

## Slide 17
Examples:
Using Two’s complement convert the following decimal numbers
into binary.
-54
-23
-101
Number Systems and Arithmetic
11001010
11101001
10011011
To Do

## Slide 18
Computer Architecture
What was covered?
Number conversions between multiple number systems.
Simple binary arithmetic.
Representing negative numbers using Two’s complement.

## Slide 19
Number Systems
Dec | Hex | Oct | Bin
0 1 2 3 4 5 6 7 8 9 10 11 12 13 14 15 | 0 1 2 3 4 5 6 7 8 9 A B C D E F | 000 001 002 003 004 005 006 007 010 011 012 013 014 015 016 017 | 00000000 00000001 00000010 00000011 00000100 00000101 00000110 00000111 00001000 00001001 00001010 00001011 00001100 00001101 00001110 00001111

## Slide 20
Computer Architecture
To Do:
Convert [base 10] 12, 15, 123, 456 & 167 to Binary
Convert [base 2] 10011, 110011, 100101 and 11100 to Decimal
Convert [base 16] A9, F2, 5A, 1F4, 2 & C9 to Decimal
Convert [base 16] A9, F2, 5A, 1F4, 2,C9 to Binary
Convert [base 10] 234, 167, 65, 23, 14 & 327 to Hexadecimal
Convert [base 8] 12, 15, 123, 456 & 167 to Decimal
Convert [base 8] 12, 15, 123, 456 & 167 to Binary
Convert [base 10] 12, 15, 123, 456 & 167 to Octal
Add [base 2] 10011 to 1001 and 11101 to 1101
Subtract [base 2] 1001 from 10011 and 1101 from 11101
Multiply [base 2] 10011 by 1001 and 11001 by 11
Using TC – Convert [base 10] -234, -15, -28, -113 & -45

## Slide 21
Computer Architecture
Next Week:
Binary Logic
Logic Gates
Boolean algebra